## Slide 1: P.L.E.D. Plaque Laser Engraving Device
Precision. Grace. Beauty. Fire.

## Slide 2: Team Members
Zachary Garrard – Hardware interfacing
  Pursuing Bachelor’s in Electrical Engineering (May 2016 Graduation)
Casey Wood – Software package design, organization
  Pursuing Bachelor’s in Electrical Engineering (May 2016 Graduation)
Justin Cox – Motor control
  Pursuing Master’s in Computer Engineering, concurrent program
Tate Shorthill – Mechanical System
  Pursuing Bachelor’s in Mechanical Engineering (May 2016 Graduation)

## Slide 3: Overview
Introduction (purpose of project)
Requirements
Specifications
System Overview Chart
Design Details
Gantt chart (schedule)
Budget
Conclusion
Questions?

## Slide 4: Project Purpose
This wood burning CNC laser engraver will:
  engrave images
  provide cheap hobbyist design
  generate software package
  provide experience

## Slide 5: Requirements
  Replicate 8 shade grayscale images
  Be contained to increase safety of bystanders
  Correct alignments errors using feedback from encoders
  Have variable laser intensity/duration control
  Have feedback control for motor positions using rotary encoders

## Slide 6: Specifications
Physical |  | Performance | 
Size | < 3 ft3 | Resolution | 85 dpi
Weight | < 30 lbs | Image | 8 shades grayscale
Power |  | Max Image Size | 1600 x 1600 pixels
Microcontroller Voltage | 5 VDC | Laser | 
Motor Driver Voltage | 18 VDC | Wavelength | 445 nm
Motor Driver Current | 3.5 A Max | Laser Driver Voltage | 5 VDC
Digital |  | Laser Diode Current | 1 – 1.7 A
Baud rate | 9600 | Optical Power | 2 W
Logic type | 5V | Power Consumption | 7.65 W

## Slide 7: System Block Diagram
s
(x,y)
(x,y)
s
(x,y)

## Slide 8: Microcontroller
  TM4C123GH6PM - TI Tiva C Launchpad
  ARM Cortex M4
  80 MHz Clock
  16 PWM Outputs
  8 UART Modules
  USB Programming/Power
  Familiarity

## Slide 9: Stepper Motors & Driver
  Input: 12-24VDC
  Max Output: 3.5 A
  Logic Level: 5V
  Microstepping for More Accuracy (1, 0.5, 0.25, 0.0625)
  Input: 2A
  Holding Torque: 0.45Nm
  200 Steps per Revolution

## Slide 10: Sensor
  Rotary Encoder
  Input: 5 – 24 V
  Output: 2 phase pulse
  Resolution
    600 pulses/rev standard
    2400 pulses/rev quadrature

## Slide 11: Laser System
2 W, 445 nm Laser
  Input: 0 – 5 V, 1 – 1.7 A
FlexMod p3 Laser Driver
  Input: PWM
  Output: 0-5 V, 1 – 1.7 A

## Slide 12: Mechanical Control System
Gantry Type | Standard | Modified | H-Bot | Core-XY | Lead Screws
Carriage (mass) | 2 | 2 | 3 | 3 | 3
Carriage (Complexity) | 2 | 2 | 2 | 3 | 3
Number of Wheels (Complexity) | 3 | 1 | 3 | 2 | 3
Movement Control (Complexity) | 3 | 3 | 2 | 2 | 3
Backlash Risk | 3 | 3 | 3 | 3 | 1
Potential Alignment Risks | 1 | 3 | 2 | 3 | 2
Tracking Speed | 3 | 3 | 3 | 3 | 1
Price (Components) | 3 | 3 | 3 | 3 | 1
Total | 20 | 20 | 21 | 22 | 17
3 is best, 1 is worst

## Slide 13: Adjusted Schedule

## Slide 14: Budget
Part | Price
Laser Diode | $70
Laser Driver | $50
Motors | $35
Encoder | $35
Motor Drivers | $30
Microcontroller | $15
Mechanical Structure | $130
Cabling, testing material | $35
Total | $400

## Slide 15: Conclusion
  Current Progress:
  Successfully testing and calibrating individual components
  Writing image processing / g-code conversion software
  Designing structure
  Foreseen Challenges:
  Structure implementation
  Pixel shade control
  Long engraving times

## Slide 16: Questions?

## Slide 17: Appendix

## Slide 18: H-Bot
Pros: light weight, clean approach, few rotating wheels, Belts avoid backlash
Cons: potential misalignments due to a moment about the carriage. Controlling two motors simultaneously

## Slide 19: Core-XY
Pros: light weight design, clean approach, belts avoid backlash, no moment about the carriage
Cons: more wheels than the H-BOT. Controlling 2 motors simultaneously

## Slide 20: Standard (one motor per axis)
Pros: Simple system.
Cons: has an inherent risk of generating a moment when arranged in simplest form

## Slide 21: Modified Standard (alternate routing)
Pros: avoid a moment thus providing better movement: each motor controls completely separate direction of movement. Simpler than H-BOT and CORE-XY
Cons: additional complexity than Standard.

## Slide 22: Lead/Ball Screw
Pro: Very simple design, each motor controls movement separately.
Con: Price, backlash. Slower tracking.