## Slide 1: P.L.E.D. Plaque Laser Engraving Device
Precision. Grace. Beauty. Fire.

## Slide 2: Team Members
Zachary Garrard – Hardware interfacing
  Pursuing Bachelor’s in Electrical Engineering (May 2016 Graduation)
Casey Wood – Software package design, organization
  Pursuing Bachelor’s in Electrical Engineering (May 2016 Graduation)
Justin Cox – Motor control
  Pursuing Master’s in Computer Engineering, concurrent program
Tate Shorthill – Mechanical System
  Pursuing Bachelor’s in Mechanical Engineering (May 2016 Graduation)

## Slide 3: Overview
Introduction (purpose of project)
Requirements
Specifications
System Overview Chart
Design Details
Gantt chart (schedule)
Budget
Conclusion
Questions?

## Slide 4: Project Purpose
This wood burning CNC laser engraver will:
  engrave images
  provide cheap hobbyist design
  generate software package
  provide experience

## Slide 5: Requirements
  Replicate 8 shade grayscale images
  Be contained to increase safety of bystanders
  Be contained to no more than 3 ft3
  Have variable laser intensity/duration control
  Have feedback control for motor position using rotary encoder

## Slide 6: Specifications
Physical |  | Performance | 
Size | < 3 ft3 | Resolution | 200 dpi
Weight | < 30 lbs | Image | 8 shades grayscale
Power |  | Max Image Size | 1600 x 1600 pixels
Microcontroller Voltage | 5 VDC |  | 
Laser Driver Voltage | 5 VDC |  | 
Laser Diode Current | 1 – 1.7 A |  | 
Motor Driver Voltage | 18 VDC |  | 
Motor Driver Current | 3.5 A Max |  | 

## Slide 7: System Overview

## Slide 8: Microcontroller
  TM4C123GH6PM - TI Tiva C Launchpad
  ARM Cortex M4
  80 MHz Clock
  16 PWM Outputs
  8 UART Modules
  USB Programming/Power
  Familiarity

## Slide 9: Stepper Motors & Driver
  Input: 12-24V, 3.5A
  Max Output: ?
  ? Logic Voltage
  Microstepping for More Accuracy (1, 0.5, 0.25, 0.0625)
  Input: 2A
  Holding Torque: 0.45Nm
  200 Steps per Revolution

## Slide 10: Sensor
  Rotary Encoder
  Input: 5 – 24 V
  Output: 2 phase pulse
  Resolution
    600 pulses/rev standard
    2400 pulses/rev quadrature

## Slide 11: Laser System
This laser system will include:
  Laser diode
  Heat sink
  Laser driver
*** Add specs for Laser and maybe replace video with pictures of laser and driver?

## Slide 12: Mechanical Structure
***Ask Tate if he can get us a decision matrix for the three types that he is deciding

## Slide 13: Proposal Schedule

## Slide 14: Adjusted Schedule

## Slide 15: Budget
Part | Price
Laser Diode | $70
Laser Driver | $50
Motors | $30
Encoder | $50
Motor Drivers | $30
Microcontroller | $20
Mechanical Structure | $125
Cabling, testing material | $25
Total | $400

## Slide 16: Conclusion
  Current Progress:
  Foreseen Challenges:
***An idea of what to put on the conclusion slide….not sure if it is what we want

## Slide 17: Questions?